## Slide 1: ORAN- MESSAGE FLOW

## Slide 3
UE Initial Access : 38.401 (NG-RAN Architecture description )
Reference : TS 138 401 - V15.5.0 pg 15

## Slide 4
5.
If UE is already registered this is provided by AMF during Paging

## Slide 6
17,18,33,

## Slide 7
INITIAL UL RRC MESSAGE – (RRC SET-UP REQUEST from UE is carried to RRC gNB through the RRC-Container field in this F1 message)

## Slide 8: PDCP entity establishment : To establish a PDCP entity for radio bearers

## Slide 9
DL RRC MESSAGE TRANSFER

## Slide 13
NAS- Message : Registration request (TS – 24.501)

## Slide 14
UL RRC MESSAGE TRANSFER

## Slide 16
INITIAL UE MESSAGE

## Slide 17
INITIAL CONTEXT SETUP REQUEST
The purpose of the Initial Context Setup procedure is to establish the necessary overall initial UE Context at the NG-RAN node, when required, including PDU session context, the Security Key, Mobility Restriction List, UE Radio Capability and UE Security Capabilities, etc.
The AMF initiates a session setup with the gNB. The message typically contains the Registration Accept NAS message. The message carries one or more PDU Session setup requests. Each PDU session is addressed with the "PDU Session ID".

## Slide 19
UE CONTEXT SETUP REQUEST (Pg-62)
The purpose of the UE Context Setup procedure is to establish the UE Context including, among others, SRB, and DRB configuration.

## Slide 22
UE CONTEXT SETUP RESPONSE (TS 38.473 Pg 65)

## Slide 23
QoS mapping when a DRB is added/modified. RRC indicates in this API if reflective QoS is used.

## Slide 24
The purpose of this message is to modify an RRC connection, e.g. to establish/modify/release RBs, to perform reconfiguration with sync, to setup/modify/release measurements, to add/modify/release SCells and cell groups. As part of the procedure, NAS dedicated information may be transferred from the Network to the UE

## Slide 26
INITIAL CONTEXT SETUP RESPONSE